## Slide 1: PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Quantities Evaluated After 6 Steps
The Collided Problem
Discretize the Collided RTE
Derive the Sweep Equations
Iterate on the Source till Convergence
Do Energy Balance
Example Plots to Show Sensitivity to Inputs
Comparison with Field Data
Interpolation

## Slide 2
What do we have now?
After Step 6 (Part One, C4-P3), we evaluated and saved the following quantities
I0(Lk,Ωo) , k = 1, 2, 3 … K+1 for direct solar radiation (downward) direction
I0(Lk,Ωnm), k = 1, 2, 3 … K+1 for all downward directions due to diffuse sky radiation
I0(Lk,Ωnm), k = 1, 2, 3 … K+1 for all upwards directions due to reflection at ground
Q1(Lk+(1/2),Ωij), k = 1, 2, 3 … K for all directions due to direct solar radiation
Q2(Lk+(1/2),Ωij), k = 1, 2, 3 … K for all directions due to diffuse sky radiation
Q3(Lk+(1/2),Ωij), k = 1, 2, 3 … K for all upwards directions due to reflection at ground
Q (Lk+(1/2),Ωij) : the sum Q1 + Q2 + Q3
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 3: PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Step 7a: The Collided Problem
where Q is the first collision source,
and S is the distributed (multiple-collision) source,

## Slide 4
Step 7b: Approximate
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
The spatial derivative IC/L as (1/ΔL) [IC(Lk+1,Ωij) - IC(Lk,Ωij)]
Cell-center collided intensity as: IC(Lk+(1/2),Ωij) = (1/2) [IC(Lk,Ωij) + IC(Lk+1,Ωij)]
We know cell-center first collision source Q(Lk+(1/2),Ωij) from previous slide
We evaluate the cell-center multiple scattering source in a similar manner, i.e.
S(Lk+(1/2),Ωij) = (1/π)  wn  wm Γ(μn,ϕm -> μi, ϕj) IC(Lk+(1/2),Ωnm)
n=1
N
m=1
m=M

## Slide 5
Step 8: Discretized RTE for Scattered Intensity
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
The LHS contains only cell-edge collided intensities
Q is already known
S is unknown but is evaluated from collided cell-center intensity
The cell-center collided intensity itself can be evaluated from cell-edge collided intensities
- μi (1/ΔL) [IC(Lk+1,Ωij) - IC(Lk,Ωij)] + G(Ωij) (1/2) [IC(Lk,Ωij) + IC(Lk+1,Ωij)] =
= Q(Lk+(1/2),Ωij) + S(Lk+(1/2),Ωij)

## Slide 6
Step 9: Derive Equations for Sweeping
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
You manipulate the discretized RTE (previous slide) to obtain:
For downward directions –
IC(Lk+1,Ωij) = aij IC(Lk,Ωij) - bij J(Lk+(1/2),Ωij)
For upward directions –
IC(Lk,Ωij) = cij IC(Lk+1,Ωij) + dij J(Lk+(1/2),Ωij)
Here J is the total source,
J(Lk+(1/2),Ωij) = Q(Lk+(1/2),Ωij) + S(Lk+(1/2),Ωij)
Set = 0.5 in the coefficients.

## Slide 7
Step 10: Iterate Until Convergence on the Multiple Scattering Source
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Evaluate S as in one of the previous slides. During the first iteration, S = 0
Evaluate total source J as Q + S
Sweep downwards. For k = 1, IC = 0 (upper boundary condition)
4) Handle lower boundary condition
5) Sweep upwards
6) Now you have an estimate of cell-edge collided intensities
7) Check for convergence
8) If iteration converged stop, else go back to Step (1)
IC(Lk=K+1,Ωij) = (ρgλ/π)  wn  wm |μn| IC(Lk=K+1,Ωnm)
n=1
n=N/2
m=1
m=M

## Slide 8
Step 11: Final
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Evaluate energy balance
Make Plots

## Slide 9
Energy Balance
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 10
BRF Angular Shape
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 11
BRF Angular Shape
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 12
Source Convergence
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 13
Reflectance as a function of LAI and Soil brightness
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Dark Soil Reflectance = 0.01
Bright Soil Reflectance = 0.3

## Slide 14
LAI Effect on Reflactance and Transmittance
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 15
Solar Polar Angle Effect on Reflactance and Transmittance
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 16
fdir Effect on Canopy Absorption
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Overcast Sky
Bright Sunny Sky

## Slide 17
Comparison with Field Data
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)

## Slide 18: PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Interpolation
Interpolation Problem:
Often you have measured Bidirectional Reflectance Factor (BRF) or HDRF in a direction ΩV that is different than the Gauss directions Ωi , i = 1, 2, …, N
You wish to compare modelled BRF with measured BRF. That means you need to evaluate the total Intensity (uncollided + collided) emerging from the canopy in the direction of measurement, ΩV
Therefore, you need to interpolate total Intensity from Gauss directions to measured direction.
The best way to do that is illustrated here, using the discrete ordinates Method
Assume you are given the measured direction (upward direction) ΩV

## Slide 19
Step 1: Evaluate Cross Sections
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
  G(ΩV)
  Γ(μO,ϕO -> ΩV)
  Γ(μn,ϕm -> ΩV)
Step 2: Evaluate Uncollided Intensity at the Ground in ΩV
Step 3: Evaluate Uncollided Intensity Emerging from the Canopy in ΩV
I0(Lk=1, ΩV) = I0(Lk=K+1, ΩV) exp [- (1/|μV| G(ΩV) LAI]
The uncollided intensity at the ground in all downward Gauss directions I0dif(Lk=K+1,Ωnm) and
I0dir(Lk=K+1,Ωo) in the above is known from the discrete-ordinates Method
I0(Lk=K+1,ΩV) = (ρgλ/π)  wn  wm |μn| I0dif(Lk=K+1,Ωnm) + (ρgλ/π) |μo| I0dir(Lk=K+1,Ωo)
n=1
n=N/2
m=1
m=M

## Slide 20
Step 4: Evaluate First Collison Source term for All Layers
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Evaluate FCS Q as Q1 + Q2 + Q3
Q1(Lk+(1/2),ΩV) = (1/π) Γ(μo,ϕo -> μV, ϕV) I0dir(Lk+(1/2), Ωo)
Q2(Lk+(1/2),ΩV) = (1/π)  wn  wm Γ(μn,ϕm -> μV, ϕV) I0dif(Lk+(1/2), Ωnm)
n=1
n=N/2
m=M
m=1
Q3(Lk+(1/2),ΩV) = (1/π)  wn  wm Γ(μn,ϕm -> μV, ϕV) I0(Lk+(1/2), Ωnm)
m=1
m=M
n=N/2+1
n = N

## Slide 21
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Step 5: Evaluate Multiple Scattering Source term for All Layers
S(Lk+(1/2),ΩV) = (1/π)  wn  wm Γ(μn,ϕm -> μV, ϕV) IC(Lk+(1/2),Ωnm)
n=1
N
m=1
m=M
The collided intensity at all cell centers in all Gauss directions IC(Lk+(1/2),Ωnm) in the
above is known from the discrete-ordinates Method (Part Two). It is evaluated as the mean of
the cell edge intensities!

## Slide 22
Step 6: Evaluate Total Source term for All Layers
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
Step 7: Evaluate Collided Intensity at the Ground in ΩV
J(Lk+(1/2),ΩV) = Q(Lk+(1/2),ΩV) + S(Lk+(1/2),ΩV)
IC(Lk=K+1, ΩV) = (ρgλ/π)  wn  wm |μn| IC(Lk=K+1,Ωnm)
n=1
n=N/2
m=1
m=M
The collided intensity at the ground in all downward Gauss directions IC(Lk=K+1,Ωnm) in the
above is known from the discrete-ordinates Method
Step 8: Sweep Upwards along Direction ΩV
Sweep upwards once to evaluate collided Intensities IC(Lk,ΩV), where k = K, K-1, K-2, …, 1
The collided intensity IC(Lk=1,ΩV) is the emerging intensity you need

## Slide 23
Step 9: Add uncollided and collided intensities
PHYSICAL MODELS IN REMOTE SENSING Chapter 04 – Part 04: Discrete Ordinates Method (Part Two)
I(Lk=1,ΩV) = I0(Lk=1,ΩV) + IC(Lk=1,ΩV)
The total intensity I(Lk=1,ΩV) is used to evaluate the BRF or HDRF and compared with the
measurement